## Slide 1: Half & Full Adder / MUX & DEMUX
Group C-FA25-BCS-C
Group Members:
Muffaser Naeem FA25-BCS-167
Amna Usman FA25-BCS-137
Isbah Waheed FA25-BCS-039
Sabahat Akbar FA25-BCS-153
Aleeza Mujeeb FA25-BCS-009

## Slide 2
HALF ADDER
Definition
• A Half Adder is a combinational circuit used to add two binary bits.
• Inputs: A and B
• Outputs: Sum and Carry
Logic Equations
Sum = A ⊕ B | Carry = A · B
Example:
1 + 1 = 10₂ → Sum = 0, Carry = 1
Quick Trick:
HALF = A + B only

## Slide 3
FULL ADDER
Definition
• A Full Adder adds three binary inputs.
• Inputs: A, B and Carry-in (Cin)
• Outputs: Sum and Carry-out (Cout)
• It can handle the carry coming from a previous addition.
Logic Equations
Sum = A ⊕ B ⊕ Cin
Cout = AB + ACin + BCin
Key Example: 1 + 1 + 1 = 11₂ → Sum = 1, Carry-out = 1
FULL = A + B + Previous Carry

## Slide 4
Binary Ripple Carry Adder & Propagation Delay
-Bit Binary Parallel Adder:
Built by cascading Full Adders (FA) in series to add two -bit binary numbers ( and ).
The carry output () of each FA is wired directly to the carry input () of the next higher stage.
The Carry Propagation Bottleneck:
The Problem: Sum cannot settle to its final value until carry ripples through all preceding stages.
Delay Calculation: Each stage adds 2 gate levels of delay Total delay = gate delays.
Impact: High bit-widths (e.g., 32-bit / 64-bit adders) severely slow down system clock speeds due to cumulative ripple delay.
Binary Ripple Carry Adder & Propagation Delay

## Slide 5
Fast Addition via Carry Lookahead Logic
Carry Lookahead Principle: Eliminates ripple delay by calculating all carry signals simultaneously in parallel.
Key Functions:
  Carry Generate (): (produces a carry output directly
  Carry Propagate (): (propagates an incoming carry)
Parallel Carry Equations:
Performance Impact: Reduces carry generation time down to just 2 gate delays across all bits regardless of adder length.

## Slide 6
What is a Binary Subtractor?
A subtractor is a combinational circuit that performs binary subtraction, generating two primary outputs: Difference (D) and Borrow (B_o). A borrow is triggered when the subtrahend bit exceeds the minuend bit (e.g., 0 - 1 requires a borrow of 1 from the next higher position).
Half Subtractor
Difference (D) 0 1 1 0 Borrow (B_o) 0 1 0 0 A Half Subtractor handles subtraction for two 1-bit numbers: minuend A and subtrahend B, without taking an incoming borrow from a previous stage.

## Slide 7
Full Subtractor
A Full Subtractor processes three 1-bit values: A (minuend), B (subtrahend), and an incoming borrow B_{in}. It is critical for multi-bit subtraction where lower positions pass generated borrows
Multi-Bit Binary Subtractor
For n-bit numbers, multiple Full Subtractors (FS) are cascaded. The borrow-out of one stage feeds directly as the borrow-in (B_{in}) of the next higher bit position, forming a ripple-borrow configuration from LSB to MSB.
Cascade Flow: FS_0 (LSB) → FS_1 → FS_2 → FS_3 (MSB)

## Slide 8
Understanding Overflow
Overflow happens when an arithmetic result exceeds the representable range for a given fixed-width bit architecture. Unsigned Subtraction
Indicated by a final active borrow. Signifies that the minuend was strictly smaller than the subtrahend.
Signed Two's-Complement Overflow Occurs in subtraction (A - B) when operands have opposite signs and the result sign differs from operand A.

## Slide 9
MULTIPLEXER: THE DIGITAL SELECTOR
MULTIPLEXER (MUX)
A Multiplexer is a combinational circuit that selects one input from multiple inputs and forwards it to a single output.
Think of MUX as a Digital Switch
I₀ ─────┐
I₁ ─────┤
I₂ ─────┤──► MUX ───► Y
I₃ ─────┘ ▲
│
Select Lines
2-to-1 MUX
A 2:1 MUX contains:
2 Data Inputs: I₀, I₁
1 Select Line: S
1 Output: Y
Select S | Selected Input | Output
0 | I₀ | Y = I₀
1 | I₁ | Y = I₁
How Does It Work?
When:
S = 0
When:
S = 1
Boolean Expression

## Slide 10
Simple Example
If:
I₀ = 1 I₁ = 0 S = 0
Then:
The MUX passes I₀ to the output.
KEY IDEA
A MUX does not process all inputs at once — it selects which input gets access to the output.

## Slide 11
MUX EXPANSION
Building a Larger MUX from Smaller MUXs
A larger MUX can be constructed by combining smaller MUXs.
4-to-1 MUX using Three 2-to-1 MUXs
MUX Selection
S₁ | S₀ | Selected Input
0 | 0 | I₀
0 | 1 | I₁
1 | 0 | I₂
1 | 1 | I₃
How Expansion Works
Stage 1: S₀ selects between:
I₀ / I₁ I₂ / I₃
Stage 2: S₁ selects one of those two results.
Therefore, 4 inputs → 1 output.
General Relationship
If a MUX has n select lines:

## Slide 12
Select Lines | Inputs
1 | 2
2 | 4
3 | 8
4 | 16
Examples:
KEY TAKEAWAY
MUX Expansion allows us to build large selection circuits using smaller MUXs.

## Slide 13
S₁ | S₀ | Selected Input
0 | 0 | I₀
0 | 1 | I₁
1 | 0 | I₂
1 | 1 | I₃
MUX (Multiplexer) Logic
A Multiplexer (MUX) is a digital circuit that selects one input from multiple inputs and sends it to a single output.
How does MUX work?
A MUX has multiple data inputs.
It has select lines that decide which input will be selected.
Only the selected input appears at the output.
Therefore, a MUX is also called a Data Selector.
Example: 4-to-1 MUX
4 Inputs: I₀, I₁, I₂, I₃ 2 Select Lines: S₀, S₁ 1 Output: Y
Main Idea: Many Inputs → MUX → One Output

## Slide 14
Enable | Output
1 | Input is passed to output
0 | Output becomes Z
Tri-State Logic
A Tri-State device is a digital circuit that can produce three possible states:
0 → LOW
1 → HIGH
Z → High Impedance
What is High Impedance (Z)?
High impedance means the output is electrically disconnected from the circuit.
It is like the device is saying:
“I am not sending 0 or 1 right now.”
Enable Control
A Tri-State buffer uses an Enable (EN) signal:
Why is it useful?
Tri-state logic allows multiple devices to share the same communication line (bus) without interfering with each other.
Main Idea:
Enable ON → 0 or 1
Enable OFF → Z

## Slide 15: THANK YOU